## Slide 1: Arduino Programming in Python
Sergio Paniego Blanco

## Slide 2: Who am I?
Artificial Intelligence MSc - UPM
sergiopaniego
sergiopaniego
sergiopaniego
Informatic Engineering and Software Enginnering - URJC
Student Developer GSoC - JdeRobot

## Slide 3: Summary
Google Summer of Code
Problematic
State of the art
PyOnArduino
Demo

## Slide 4: Google Summer of Code
Global program
Timeline
February - Organizations announced
March - Student applications
April – Student Projects announced
April & May – Community Boarding
May to August – Coding
June, July & August - Evaluations
JdeRobot – 6 students
Bring students into open source development
Remote work + meetings

## Slide 5: Problematic
Arduino programming language complexity
Need of easy to use tools for newbies
Code Arduino boards using Python

## Slide 6: State of the art
Current solution for the problematic
Continuous communication between the robot and the PC.
Possible approaches
Pyxie
Cython
LLVM

## Slide 8: PyOnArduino
JdeRobot Robot Programming tool
Translate Python-like code to Arduino code
People:
José María Cañas
Gorka Guardiola
Luis Roberto Morales
Sergio Paniego Blanco
Translate, compile and upload the code directly

## Slide 10: Supported robots
MBOT
COMPLUBOT

## Slide 11: PyOnArduino’s structure

## Slide 13: Translator
Abstract Syntax Tree
Each node – Statement in the code
Information for analyzing the code
Inessential puntuation and delimiters
Python library
NodeTransformer and NodeVisitor

## Slide 14: Abstract Syntax Tree
while b ≠ 0
if a > b
a := a − b
else
b := b − a
return a
Greatest Common Divisor

## Slide 15: Translator
Abstract Syntax Tree
Each node – Statement in the code
Information for analyzing the code
Python library
NodeTransformer and NodeVisitor

## Slide 16
import ast
class MyVisitor(ast.NodeVisitor): def visit_Str(self, node): print('String Node: "' + node.s + '"') class MyTransformer(ast.NodeTransformer): def visit_Str(self, node): return ast.Str('str: ' + node.s)
parsed = ast.parse("print('Hello World’)”)
MyTransformer().visit(parsed) MyVisitor().visit(parsed)
NodeVisitor & NodeTransformer

## Slide 17: HALduino
Hadware Abstraction Layer
halduino.py
Specific halduino for each robot
Get rid of Arduino’s complexity

## Slide 18: HALduino example
setSpeedEngines(leftSpeed: int, rightSpeed: int)
MeDCMotor leftMotor(9); MeDCMotor rightMotor(10); void setSpeedEngines(int speedLeft, int speedRight) { leftMotor.run(speedLeft); rightMotor.run(speedRight); }
Python
Arduino

## Slide 19: Sensors and actuators supported
Sensor/Actuator | Supported functions
DC Engines | setSpeedEngines (left,right)
Ultrasonic sensors | getUS()
Infrared sensors | getIR[1,2,3,4,5]()
Beep emitter | playBeep(type)
Sound emitter | playMelody(melody)
Screen write | setScreenText(text), cleanScreen()
Complubot

## Slide 20: Sensors and actuators supported
Sensor/Actuator | Supported functions
DC Engines | setSpeedEngines (speed)
Ultrasonic sensors | getUS()
LEDs | setLeds(ledNumber, red, green, blue)
Infrared sensors | getMessage(), sendMessage(message)
Light sensor | getLightSensor()
Button | isButtonPressed(), isButtonReleased()
Buzzer | playBuzzer(tone, length)
External screen | drawString(name), showClock(hour, min)
mBot

## Slide 21: Python features supported
Feature | Limitations/Comments
Variable declaration | SUPPORTED
Function declaration | With/without return statement
Operators | + - / * ^ %
Comparators | < <= >= == !=
Logic operators | And or is not
pass | SUPPORTED
loops | While, for(limited)
Sleep() | SUPPORTED
if | If/elif/else
Boolean operations | and or
print | SUPPORTED

## Slide 22: Stop and go code example Mbot
import HALduino.halduino as halduino def set_engine(direction: int): if direction == 0: halduino.setSpeedEngines(0, 0) print('STOP!') elif direction == 1: halduino.setSpeedEngines(100, 100) print('Forward') def loop(): if halduino.getUS() < 10: set_engine(0) else: set_engine(1)

## Slide 23: Stop and go code example Complubot
import HALduino.halduino as halduino def set_engine(direction: int): if direction == 0: halduino.setSpeedEngines(0, 0) print('STOP!') elif direction == 1: halduino.setSpeedEngines(100, 100) print('Forward') def loop(): if halduino.getUS() < 30: set_engine(0) else: set_engine(1)

## Slide 24: Managing robot’s architecture
Versatility
# Example of an mBot setup leftMotor = 9 rightMotor = 10 ultrasonicSensor = 3 rgbled = 7 lightSensor = 6 ledMtx = 3 lineFollower = 2
Configure robot’s ports

## Slide 25: Executing PyOnArduino
Python 3.x
python3 translator/Translator.py [input-file] [robot]
python3 translator/Translator.py [input-file] [robot] [architecture-file]
Arduino IDE
Arduino Makefile

## Slide 26: Make & Arduino Makefile
Build automation
# mBot Makefile ARDUINO_LIBS= Makeblock-Libraries-master Wire SPI MONITOR_PORT= /dev/cu.wchusbserial1420 BOARD_TAG = uno ARDUINO_DIR = /Applications/Arduino.app/Contents/Java include /usr/local/opt/arduino-mk/Arduino.mk
Directives used by make
make upload

## Slide 27: Problems during development
Dynamic typing in Python vs Arduino
Architectural Stop
Variables’ type in function declaration
Lost parentheses

## Slide 28: DEMO TIME!
Lets see how PyOnArduino tool works!

## Slide 30: Thanks!
Any questions?
You can find me at @sergiopaniego